## Slide 1: Week 1 Class 2
Reference Frames

## Slide 2: Reference Frames
In guidance and control of aircraft, reference frames used a lot
Describe relative position and orientation of objects
  Aircraft relative to direction of wind
  Camera relative to aircraft
  Aircraft relative to inertial frame
Some things most easily calculated or described in certain reference frames
  Newton’s law
  Aircraft attitude
  Aerodynamic forces/torques
  Accelerometers, rate gyros
  GPS
  Mission requirements
Must know how to transform
between different reference
frames

## Slide 3: Rotation of Reference Frame
Notes: \textbf{p} = p_x^0 \textbf{i}^0 + p_y^0 \textbf{j}^0 + p_z^0 \textbf{k}^0
\textbf{p} = p_x^1 \textbf{i}^1 + p_y^1 \textbf{j}^1 + p_z^1 \textbf{k}^1
p_x^1 \textbf{i}^1 + p_y^1 \textbf{j}^1 + p_z^1 \textbf{k}^1 = p_x^0 \textbf{i}^0 + p_y^0 \textbf{j}^0 + p_z^0 \textbf{k}^0
\textbf{p}^1 \stackrel{\triangle}{=} \begin{pmatrix}
p_x^1 \\
p_y^1 \\
p_z^1
\end{pmatrix} = \begin{pmatrix}
\textbf{i}^1 \cdot \textbf{i}^0 & \textbf{i}^1 \cdot \textbf{j}^0 & \textbf{i}^1 \cdot \textbf{k}^0 \\
\textbf{j}^1 \cdot \textbf{i}^0 & \textbf{j}^1 \cdot \textbf{j}^0 & \textbf{j}^1 \cdot \textbf{k}^0 \\
\textbf{k}^1 \cdot \textbf{i}^0 & \textbf{k}^1 \cdot \textbf{j}^0 & \textbf{k}^1 \cdot \textbf{k}^0
\end{pmatrix} \begin{pmatrix}
p_x^0 \\
p_y^0 \\
p_z^0
\end{pmatrix}
\textbf{p}^1 = \mathcal{R}_0^1 \textbf{p}^0
Where
\mathcal{R}_0^1 \stackrel{\triangle}{=} \begin{pmatrix}
\cos\theta & \sin\theta & 0 \\
-\!\sin\theta & \cos\theta & 0 \\
0 & 0 & 1
\end{pmatrix}
(rotation about $\textbf{k}$ axis)

## Slide 4: Rotation of Reference Frame
Notes: \noindent
Right-handed rotation about $\textbf{j}$ axis:
\[
\mathcal{R}_0^1 \stackrel{\triangle}{=} \begin{pmatrix}
\cos\theta & 0 & -\!\sin\theta \\
0 & 1 & 0 \\
\sin\theta & 0 & \cos\theta
\end{pmatrix}
\]
\noindent
Right-handed rotation about $\textbf{i}$ axis:
\[
\mathcal{R}_0^1 \stackrel{\triangle}{=} \begin{pmatrix}
1 & 0 & 0 \\
0 & \cos\theta & \sin\theta \\
0 & -\!\sin\theta & \cos\theta
\end{pmatrix}
\]
\noindent
Orthonormal matrix properties:
\begin{itemize}
\item[{\bf P.1.}] $(\mathcal{R}_a^b)^{-1} = (\mathcal{R}_a^b)^{\top} = \mathcal{R}_b^a$
\item[{\bf P.2.}] $\mathcal{R}_b^c \mathcal{R}_a^b = \mathcal{R}_a^c$
\item[{\bf P.3.}] $\det\!\left(\mathcal{R}_a^b\right) = 1$
\end{itemize}

## Slide 5: Rotation Formula

## Slide 6: Rotation Formula

## Slide 7: Rotation Formula

## Slide 8: Inertial Frame and Vehicle Frame
Notes: \begin{itemize}
\item Vehicle frame has same orientation
as inertial frame
\item Vehicle frame is fixed at cm of aircraft
\item Inertial and vehicle frames are referred
to as NED frames
\item $N \longrightarrow x$, $E \longrightarrow y$, $D \longrightarrow z$
\end{itemize}

## Slide 9: Euler Angles
Need way to describe attitude of aircraft
Common approach: Euler angles
Pro: Intuitive
Con: Mathematical singularity
  Quaternions are alternative for overcoming singularity
Notes: $\psi$: heading (yaw)
\vspace{.5cm}
$\theta$: elevation (pitch)
\vspace{.5cm}
$\phi$: bank (roll)

## Slide 10: Vehicle-1 Frame
Notes: \[
\mathcal{R}_v^{v1}(\psi) =
\begin{pmatrix}
\cos\psi & \sin\psi & 0 \\
-\sin\psi & \cos\psi & 0 \\
0 & 0 & 1
\end{pmatrix}
\]
gives
\[
\mathbf{p}^{v1} = \mathcal{R}_v^{v1}(\psi) \mathbf{p}^v
\]
where $\psi$ is the heading.

## Slide 11: Vehicle-2 Frame
Notes: \renewcommand{\textwidth}{2in}
\[
\mathcal{R}_{v1}^{v2}(\theta) =
\begin{pmatrix}
\cos\theta& 0 & -\sin\theta \\
0 & 1 & 0 \\
\sin\theta & 0 & \cos\theta
\end{pmatrix}
\]
gives
\[
\mathbf{p}^{v2} = \mathcal{R}_{v1}^{v2}(\theta) \mathbf{p}^{v1}
\]
where $\theta$ is the pitch angle.

## Slide 12: Body Frame
Notes: \renewcommand{\textwidth}{2in}
\[
\mathcal{R}_{v2}^{ b}(\phi) =
\begin{pmatrix}
1 & 0 & 0 \\
0 & \cos\phi & \sin\phi \\
0 & -\sin\phi & \cos\phi
\end{pmatrix}
\]
gives
\[
\mathbf{p}^{b} = \mathcal{R}_{v2}^{ b}(\phi) \mathbf{p}^{v2}
\]
where $\phi$ is the roll (bank) angle.

## Slide 13: Inertial Frame to Body Frame Transformation
Notes: \newcommand{\cth}{c_{\theta}}
\newcommand{\sth}{s_{\theta}}
\newcommand{\cps}{c_{\psi}}
\newcommand{\sps}{s_{\psi}}
\newcommand{\cph}{c_{\phi}}
\newcommand{\sph}{s_{\phi}}
Define
\begin{align*}
\mathcal{R}_{v}^{ b}(\phi,\theta,\psi) &= \mathcal{R}_{v2}^{b}(\phi) \mathcal{R}_{v1}^{v2}(\theta) \mathcal{R}_{v}^{v1}(\psi) \\
&=
\begin{pmatrix}
1 & 0 & 0 \\
0 & \cos\phi & \sin\phi \\
0 & -\sin\phi & \cos\phi
\end{pmatrix}
\begin{pmatrix}
\cos\theta& 0 & -\sin\theta \\
0 & 1 & 0 \\
\sin\theta & 0 & \cos\theta
\end{pmatrix}
\begin{pmatrix}
\cos\psi & \sin\psi & 0 \\
-\sin\psi & \cos\psi & 0 \\
0 & 0 & 1
\end{pmatrix} \notag \\
&=
\begin{pmatrix}
\cth \cps & \cth \sps & -\sth \\
\sph \sth \cps - \cph \sps & \sph \sth \sps + \cph
\cps & \sph \cth \\
\cph \sth \cps + \sph \sps & \cph \sth \sps - \sph
\cps & \cph \cth
\end{pmatrix}
\end{align*}
to give
\[
\textbf{p}^{b} = \mathcal{R}_{v}^{b}(\theta) \textbf{p}^{v}
\]

## Slide 14: Stability Frame
Stability frame helps us rigorously
define angle of attack and is useful
for analyzing stability of aircraft
Notes: \mathcal{R}_{b}^{s}(\alpha) =
\begin{pmatrix}
\cos\alpha & 0 & \sin\alpha \\
0 & 1 & 0 \\
-\sin\alpha & 0 & \cos\alpha
\end{pmatrix}
\mathbf{p}^{s} = \mathcal{R}_{b}^{s}(\alpha) \mathbf{p}^{b}

## Slide 15: Wind Frame
Notes: \mathcal{R}_{s}^{w}(\beta) =
\begin{pmatrix}
\cos\beta & \sin\beta & 0 \\
-\sin\beta & \cos\beta & 0 \\
0 & 0 & 1
\end{pmatrix}
\mathbf{p}^{w} = \mathcal{R}_{s}^{w}(\beta) \mathbf{p}^{s}
\mathcal{R}_{b }^{w}(\alpha,\beta) &= \mathcal{R}_{s}^{w}(\beta) \mathcal{R}_{b}^{s}(\alpha)\\
&= \begin{pmatrix}
\cos\beta & \sin\beta & 0 \\
-\sin\beta & \cos\beta & 0 \\
0 & 0 & 1
\end{pmatrix}
\begin{pmatrix}
\cos\alpha & 0 & \sin\alpha \\
0 & 1 & 0 \\
-\sin\alpha & 0 & \cos\alpha
\end{pmatrix} \\
&= \begin{pmatrix}
\cos\beta\cos\alpha & \sin\beta & \cos\beta\sin\alpha \\
-\sin\beta\cos\alpha & \cos\beta & -\sin\beta\sin\alpha \\
-\sin\alpha & 0 & \cos\alpha
\end{pmatrix}

## Slide 16: Wind Frame (continued)
Wind frame helps us rigorously define side-slip angle
Side-slip angle is nominally zero for tailed aircraft
Notes: \mathcal{R}_{w}^{b}(\alpha,\beta) = (\mathcal{R}_{b}^{w})^{\top}(\alpha,\beta) =
\begin{pmatrix}
\cos\beta\cos\alpha & -\sin\beta\cos\alpha & -\sin\alpha \\
\sin\beta & \cos\beta & 0 \\
\cos\beta\sin\alpha & -\sin\beta\sin\alpha & \cos\alpha
\end{pmatrix}

## Slide 17: Airspeed, Wind Speed, Ground Speed
ground track
a/c wrt to inertial frame
expressed in body frame
wind wrt to inertial frame
expressed in body frame
a/c wrt to surrounding air
expressed in body frame
Notes: \begin{align*}
\mathbf{V}_a &= \mathbf{V}_g - \mathbf{V}_w
\\
\mathbf{V}_g^b &= \begin{pmatrix} u \\ v \\
w\end{pmatrix}
\\
\mathbf{V}_w^b &= \begin{pmatrix} u_w \\ v_w \\ w_w\end{pmatrix} =
\mathcal{R}_{v}^{b}(\phi,\theta,\psi)
\begin{pmatrix} w_n \\ w_e \\ w_d \end{pmatrix}
\\
\mathbf{V}_a^w &= \begin{pmatrix} V_a \\ 0 \\
0\end{pmatrix}
\\
\mathbf{V}_a^b &= \begin{pmatrix} u_r \\ v_r \\ w_r \end{pmatrix} =
\begin{pmatrix} u - u_w \\ v - v_w \\ w - w_w \end{pmatrix}
\end{align*}

## Slide 18: Airspeed, Angle of Attack, Sideslip Angle
Notes: \mathbf{V}_a^b &= \begin{pmatrix} u_r \\ v_r \\ w_r \end{pmatrix} =
\mathcal{R}_{w}^{b}
\begin{pmatrix} V_a \\ 0 \\ 0 \end{pmatrix}
\\
&= \begin{pmatrix}
\cos\beta\cos\alpha & -\sin\beta\cos\alpha & -\sin\alpha \\
\sin\beta & \cos\beta & -\sin\beta\sin\alpha \\
\cos\beta\sin\alpha & 0 & \cos\alpha
\end{pmatrix} \begin{pmatrix} V_a \\ 0 \\ 0 \end{pmatrix}
\begin{pmatrix} u_r \\ v_r \\ w_r \end{pmatrix} =
V_a \begin{pmatrix} \cos\alpha \cos\beta \\ \sin\beta
\\ \sin\alpha\cos\beta \end{pmatrix}
V_a &= \sqrt{u_r^2 + v_r^2 + w_r^2} \notag \\
\alpha &= \tan^{-1}\left(\frac{w_r}{u_r}\right) \label{eq:frames-Valphabeta-to-uvw} \\
\beta &= \sin^{-1}\left( \frac{v_r}{\sqrt{u_r^2+v_r^2+w_r^2}} \right)

## Slide 19: Course and Flight Path Angles
Flight path projected onto ground
horizontal component
of groundspeed vector
Notes: $\gamma$: flight path angle
$\chi$: course angle

## Slide 20: Wind Triangle
ground track
north
Notes: $\chi$: course angle
$\psi$: heading angle
$\beta$: side slip angle
$\chi_c$: crab angle
$\chi_w$: wind direction
\chi_c \defeq \chi - \psi

## Slide 21: Wind Triangle
Notes: $\theta$: pitch angle
$\alpha$: angle of attack
$\gamma$: flight path angle
$\gamma_a$: air-mass-relative flight path angle
\gamma_a = \theta-\alpha

## Slide 22: When wind speed and sideslip are zero…
Notes: If both the windspeed and the sideslip angles are zero, i.e.,
\begin{align*}
V_w &= 0 \\
\beta &= 0
\end{align*}
then we have the following simplifications
\begin{align*}
V_a &= V_g \text{~~~Airspeed equals groundspeed} \\
u &= u_r \text{~~~Velocity equals velocity relative to the air mass}\\
v &= v_r \\
w &= w_r \\
\psi &= \chi \text{~~~Heading equals course} \\
\gamma &= \gamma_a \text{~~~Flight path angle equals air-mass-referenced flight path angle}
\end{align*}

## Slide 23: Equation of Coriolis
Notes: \mathbf{p} &= p_x \mathbf{i}^b + p_y \mathbf{j}^b + p_z \mathbf{k}^b
\\
\frac{d}{dt_i}{\mathbf{p}} &= \dot{p}_x \mathbf{i}^b + \dot{p}_y \mathbf{j}^b + \dot{p}_z \mathbf{k}^b
+ p_x \frac{d}{dt_i}\mathbf{i}^b + p_y \frac{d}{dt_i}\mathbf{j}^b + p_z \frac{d}{dt_i}\mathbf{k}^b
\\
\frac{d}{dt_b}\mathbf{p} &= \dot{p}_x \mathbf{i}^b + \dot{p}_y \mathbf{j}^b + \dot{p}_z \mathbf{k}^b
\\
\dot{\mathbf{i}}^b &= \boldsymbol{\omega}_{b/i} \times \mathbf{i}^b \\
\dot{\mathbf{j}}^b &= \boldsymbol{\omega}_{b/i} \times \mathbf{j}^b \\
\dot{\mathbf{k}}^b &= \boldsymbol{\omega}_{b/i} \times \mathbf{k}^b \\
p_x \dot{\mathbf{i}}^b &+ p_y \dot{\mathbf{j}}^b + p_z \dot{\mathbf{k}}^b
= p_x (\boldsymbol{\omega}_{b/i} \times \mathbf{i}^b)
+ p_y (\boldsymbol{\omega}_{b/i} \times \mathbf{j}^b)
+ p_z (\boldsymbol{\omega}_{b/i} \times \mathbf{k}^b) \nonumber \\
&\qquad\qquad\qquad = \boldsymbol{\omega}_{b/i} \times \mathbf{p}
\\
\frac{d}{dt_i}\mathbf{p} &= \frac{d}{dt_b}\mathbf{p} + \boldsymbol{\omega}_{b/i}
\times\mathbf{p}

## Slide 24: Material Covered
Section 1 of note “Quadrotor Dynamics and Control”
Chapter 2 of book “Small Unmanned Aircraft”